## Slide 1
Carrier Reliability and Dynamic LLR Scale
Core receiver calculation
1
Quality
rₖ = |Hₖ|²
────────
eₖ
signal gain / training error
→
2
Reference
rᵣₑ𝒻 =
medianₖ(rₖ)
one reference for all carriers
→
3
Normalize
qₖ = rₖ
──────
rᵣₑ𝒻
relative carrier quality
→
4
Scale
sₖ = b ·
clip(√qₖ,
0.25, 4)
square root limits the change
b = 3, eₘₑ𝒹 ≤ 1
b = clip(3 / √eₘₑ𝒹, 0.5, 3), eₘₑ𝒹 > 1
eₘₑ𝒹 = medianₖ(eₖ)
rₖ > rᵣₑ𝒻 ⇒ sₖ > b | rₖ < rᵣₑ𝒻 ⇒ sₖ < b
Notes: The slide shows only the four formulas used to turn carrier quality into a dynamic LLR scale. The receiver computes r_k, takes its median, divides by that median, takes the square root, and multiplies by the base scale b. Weak carriers get a smaller scale; reliable carriers get a larger scale.