## Slide 1
Dynamic LLR Scale
Receiver-side calculation after SFO correction
After SFO correction:
Yᶜᵒʳʳₘ,ₖ = Hₖ Xₘ,ₖ + Nₘ,ₖ
m = training symbol k = active carrier
1 Channel estimate
Ĥₖ = Σₘ X*ₘ,ₖ Yᶜᵒʳʳₘ,ₖ
───────────────
Σₘ |Xₘ,ₖ|²
2 Training residual
eₖ = (1/M) Σₘ
|Yᶜᵒʳʳₘ,ₖ − ĤₖXₘ,ₖ|²
eₘₑ𝒹 = medianₖ(eₖ)
3 Carrier reliability
rₖ = |Ĥₖ|² / max(eₖ, ε)
rᵣₑ𝒻 = medianₖ(rₖ)
wₖ = clip(√(rₖ/rᵣₑ𝒻), 0.25, 4)
4 Dynamic scale
b = 3, eₘₑ𝒹 ≤ 1
b = clip(3/√eₘₑ𝒹, 0.5, 3), eₘₑ𝒹 > 1
sₖ = b · wₖ
Equalize
Zₘ,ₖ = Yᶜᵒʳʳₘ,ₖ / Ĥₖ
→
LLR for QPSK
Lₖ,₁ = sₖ · Im(Zₘ,ₖ)
Lₖ,₂ = sₖ · Re(Zₘ,ₖ)
→
LDPC
Lᵖᵒˢᵗ = Lᶜʰ + parity messages
bit = sign(Lᵖᵒˢᵗ)
→
Result
BER after LDPC = 0%
JPG recovered
Fixed baseline: sₖ = 3 for every carrier
Adaptive: weak carrier ↓ confidence | reliable carrier ↑ confidence
Notes: English speaker script
This slide shows how we calculate the dynamic LLR scale. First, we correct the SFO phase. For each training carrier, we estimate the channel H from the known training signal. Then we measure the residual error e. A small residual means a better carrier.
Next, we use r equals channel gain squared divided by the residual. We compare each r with the median value. This gives a relative carrier weight. We also calculate a base scale. The base scale is 3 when the median error is small. When the median error is above 1, we use 3 divided by the square root of the median error, with limits from 0.5 to 3.
The final scale for carrier k is the base scale times its weight. We use this scale for the two LLR values from each QPSK carrier. The LDPC decoder then uses the LLR values and the parity checks. With this change, the BER after LDPC became zero, and we recovered the JPG.
中文演讲稿
这一页说明动态 LLR scale 是怎样计算的。首先，我们先校正 SFO 带来的相位变化。对于每一个 training 载波，我们根据已知的 training 信号估计信道 H，然后计算残差 e。残差越小，说明这个载波越可靠。
接着，我们使用“信道增益的平方除以残差”得到可靠度 r，再把每个载波的 r 和所有载波的中位数进行比较，从而得到相对权重。同时，我们计算基础 scale。当中位数误差较小时，基础 scale 取 3；当中位数误差大于 1 时，使用 3 除以中位数误差的平方根，并把结果限制在 0.5 到 3 之间。
最后，第 k 个载波的 scale 等于基础 scale 乘以它自己的权重。这个 scale 会用于该 QPSK 载波产生的两个 LLR。LDPC 再利用这些 LLR 和奇偶校验关系进行解码。改进后，LDPC 后 BER 达到 0%，原始 JPG 成功恢复。